## Slide 1
Aquaponics in CEA
Matthew “Rex” Recsetar, PhD
Assistant Professor Biosystems Engineering, Extension Specialist
© 2025 Matthew Recsetar

## Slide 2: What is Aquaponics?
Combination of:
Aquaculture: farming of aquatic organisms under controlled conditions
Hydroponics: cultivation of plants in nutrient-rich soilless systems

## Slide 3: Is Aquaponics a New Technology?
No, not really
  Dates back 3,000 years
  Mesoamerica
    Artificial islands or floating gardens
    Layered mud on top of buoyant materials in shallow lakes or wetlands
  China
    Culture of fish in rice paddies
Modern aquaponics: ~40 years
  James Rakocy (University of Virgin Islands – 1980s)

## Slide 4: Aquaponics is Not Just a Production System
It is a platform for:
Circular Nutrient Management
Biological Innovation
Waste Valorization
New Revenue Streams

## Slide 5: Why does it work?

## Slide 6
The Aquaponic Cycle
Fish produce wastes
Microbes convert wastes to fertilizer (nutrients) for plants
Plants filter water that is returned to the fish
Nutrient Rich Effluent
Feces + NH3

## Slide 7: Aquaponics Process Diagram
*Composting Unit = Sludge Digestion
Photo Credit: Ragnheidur Thorarinsdottir
+Alkalinity

## Slide 8
Why is Aquaponics Considered Sustainable?
  Resource use efficiency
    Free nutrients through fish feed – majority of salts don’t have to be mined or produced in a lab
    Uses less water than soil-based or hydroponic plant production
  No runoff and limited discharge into environment
    Even the best RAS discharges significant amounts of effluent daily
  Organic plant production possible
    Reduced chemical input
    Healthier Product
  Local and year-round production

## Slide 9: Where Aquaponics is Truly Sustainable (and where it isn’t yet)
Strengths
Water Reuse
Nutrient Recovery from Waste Streams
Reduced Synthetic Fertilizer Dependence
Potential Circularity
Limitations
Energy Use (pumps, heating, lighting)
Capital Intensive
Fish Feed Sourcing
Nutrient Imbalances
Notes: So aquaponics isn’t automatically sustainable.

## Slide 10: Closing the Loop in Aquaponics
Feed Input (External)
Fish
Waste (Solids + Dissolved Nutrients)
Reuse Pathways
Plants (Nutrient Uptake)
Solids/Effluent Streams
Nutrient Factory
(Natural Process)
Lost if not mineralized
Often Discharged
Where Innovation Happens
Notes: The next step is figuring out how we actually close the loop. Most aquaponics systems are not circular, they’re just less wasteful.

## Slide 11: Why Use Aquaponics?

## Slide 12: Shifting Trends in food markets
Consumers are increasingly looking for ways to reduce their environmental impact – creating increased niche for sustainably grown foods
Increased demand for locally grown foods – perceived as fresher and tastier
Demand for organic foods – has been increasing at a steady rate since 2012

## Slide 13: Key Advantages of Aquaponics
Water Efficiency (30%-60% less water than hydroponics)
Reduces Synthetic Fertilizer Use
Integrated Production
Potential Microbiome Benefits
Year-round production

## Slide 14: Advantages of Aquaponics
Provides nutrient rich effluent to hydroponically grown plants (no fertilizers needed)
Nutrients considered organic
Adequate nutrients available when allowed to build up in aquaculture system
Micros

## Slide 15: Where Aquaponics has a Unique Advantage
Microbiome driven plant performance (Diverse and complex bacterial load in)
Nutrient recycling vs hydroponics
Waste >> Revenue Potential

## Slide 16: Three Traditional Aquaponic System Types
Media Bed System
  Can be Flood and Drain or Ebb and Flow system, flow through or standing water level
Deep Water Culture (DWC) or Raft System
Nutrient Film Technique (NFT)

## Slide 17: Dutch Buckets/Bato Buckets
Most common in commercial aquaponics for fruited plants

## Slide 18: How Do We Make Aquaponics Work in CEA?
Decoupling
Nutrient Control
Crop Selection

## Slide 19: Decouple the System to optimize plant production
Photo Credit: Ragnheidur Thorarinsdottir

## Slide 20: Fish Don’t Have to be for Food
Also, for aesthetics (ornamentals), baitfish or just for nutrients!

## Slide 21: Aquaponics = Nutrient Factory
Optimize aquaculture system to produce the best nutrient concentration for plants you are growing
Allow pH to run low (6.0-6.5)
Supplement alkalinity and boost pH with potassium bicarbonate and calcium carbonate
Made possible through mineralization of fish waste
Notes: This is how we close the loop

## Slide 22: Mineralization of Sludge
Extraction of nutrients from solids removed from aquaculture system
Aerobic bacterial action like aeration basins in wastewater treatment plants
Crucial Step!

## Slide 23: Aerobic Mineralization
Process whereby solid fish waste (poop, uneaten feed) is broken down and converted to mineral forms that can be utilized by plants as nutrients
  Aerobic (preferred) – relies on bacteria (and other microbes) to break down the solids through mixing and aeration
    Faster degradation of organic solids
  Typically, 4 weeks total retention time needed (often in 2 stages)
Notes: Nutrients in solids are unavailable to plants so must be broken down (mineralized)

## Slide 24: Sludge Tank While Aerated Vs After Settling
*Typically >1 hour required for settling, then 2nd stage mineralization supernatant added directly back to RAS

## Slide 25
Mineralization Experiment Showed
  Phosphate (PO₄³⁻) = 16.5% increase after 2 weeks; 45.0% increase after 4 weeks
  Potassium (K⁺) = 20.4% increase after 2 weeks; 31.5% increase after 4 weeks
  Calcium (Ca²⁺)= 25.5% increase after 2 weeks; 59.4% increase after 4 weeks
  Magnesium (Mg²⁺) = 14.6% increase after 2 weeks; 42.1% increase after 4 week
  Boron (B) = 30.0% increase after 2 weeks; 90% increase after 4 weeks
  Manganese (Mn) = 41.7% increase after 2 weeks; 96.3% increase after 4 weeks

## Slide 26: Adding Mineralized Water Back into RAS Allows you to Build System Nutrients over Time
Estimate running system for 3 months minimum to achieve desired nutrient gradients
Circularity

## Slide 27
What about Aquaculture Biosolid Production
  Produced through dehydrating incomplete mineralized sludge
    Why is it incomplete?
      Strong Organic bonds
    Stabilized solids can build up over time in a mineralization system
    Eventually removed and dewatered
      Sun drying, air drying (time), geotextile bags
  Benefit over non-stabilized fish waste solids
    Stable
    No smell
    Promotes controlled nutrient release in soil and reduced oxygen demand
    Improves soil structure

## Slide 28
Aquaculture Biosolids Experiment
  Demonstrate efficacy of aquaculture biosolids for growing Durum Wheat
    Compared to granular fertilizer and dairy manure
    Examine soil nutrient content, moisture content, yield, protein and soil productivity

## Slide 29
Aquaculture Biosolid Performance
  Comparable Yields to other treatments but higher protein content
  Improved soil health through addition of carbon, sulfur and microbes
  More research needed, but results were promising
  Will be important to assess the economic feasibility of attaining and using large quantities on a commercial scale

## Slide 30
How We Improve Sustainability (and Profitability)
  Effluent Reuse
    External irrigation to fruit trees or other crops or sell to hydroponic growers
  Biosolids
    Collection of stabilized biosolids for use in land-based agriculture or gardens
  Integration

## Slide 31
Effluent Sales
  Typically, mineralized water depending on concentration of system water
  Have been able to consistently show that 10% effluent can reduce water usage in hydroponic hemp production and potentially improve bud quality through root microbial interactions
  It isn’t just the nutrients!
    Effluent from Mineralized Solids contains good microbes for inoculating root zones in hydroponic systems
  $75/gallon in niche high-value systems
    i.e. Cannabis

## Slide 32
Sustainable Fruit Orchard Project
  Demonstration of how trees can be grown more sustainably with effluent and biosolids from aquaculture systems
  Smart irrigation + Rainwater harvesting

## Slide 33: The Microbiome Advantage
This is what hydroponics lacks
This is where innovation is happening
Improves nutrient uptake and plant resilience

## Slide 34: Active Nutrient Management in Aquaponics
Allows for RAS to achieve adequate nutrient levels for high-nutrient demand crops
Examined: Flow through vs recirculating vs hybrid systems vs hydroponics
Flow through and hybrid systems had Equivalent yields to hydroponic control
Water Savings (~60%)
Dutch Bucket Cannabis

## Slide 35
*Attribute success to root microbiome introduced from aquaculture effluent

## Slide 36: How Does Introducing a Microbiome Benefit the Plants?
Phytohormones - Beneficial microbes (PGPMs) synthesize phytohormones like auxins and gibberellins, which stimulate root development and improve nutrient absorption
Enhancement of Root Exudates – Chemical signaling directs microbes to make things plants want or to release compounds that recruit specific microbes
Phosphorous Solubilization – Specific bacteria convert insoluble phosphorus to soluble forms, increasing solubility to plants

## Slide 37
How does Sustainability Drive Profits?
People will pay more for eco-friendly products
Deeper brand loyalty – repeat customers
Reducing water, nutrient and energy costs can lower operational costs and improve profit margins
Additional revenue streams through waste products
Employee engagement and retention
Younger people want to work for companies with strong commitments to sustainability
Long-term stability

## Slide 38: Currently only a few Commercially Viable Aquaponic Businesses Exist…but why?

## Slide 39: Reasons Why Many Commercial Aquaponics Farms Fail?
Focus too heavily on fish production
High capital and Operating costs
Poorly designed systems
Marketing issues
  Underselling product, not understanding market
Poor nutrient management
Increased complexity
  Lack of necessary skills to manage and operate

## Slide 40: Large Aquaponics Farms that Have Gone out of Business in Recent Years
The FishFarmers (USA) - Based in Florida, The FishFarmers was one of the largest aquaponic operations in the country, but they shut down in the mid-2010s. They faced financial difficulties due to low demand for their products and issues with scaling their aquaponics technology.
Aquaponics USA (USA) - Located in Florida, Aquaponics USA was one of the prominent early players in the industry. The company shut down operations in the 2010s after struggling with financial sustainability, production inefficiencies, and market adoption.
Gotham Greens (USA) - While Gotham Greens, an urban farming operation that uses hydroponics, remains active, it faced difficulties with its aquaponic operations. Their original aquaponics facility in New York City had to scale back in the early 2010s due to the high cost of operation, and the focus shifted away from aquaponics in favor of other hydroponic techniques.
Aqua Vita Farms (USA) - Based in California, Aqua Vita Farms was an ambitious aquaponics project that ultimately went out of business due to financial difficulties and inconsistent market demand. Their attempt to create a large-scale, commercial aquaponics operation proved unsustainable.
Dayton Valley Aquaponics (USA) - This large-scale operation outside of Reno Nevada shut down in 2021 due to shifting markets during the pandemic, high operational costs and scaling difficulties. They utilized a coupled aquaponics system.
Green Sky Growers (USA) - Green Sky Growers in Florida, which operated large-scale aquaponic systems, faced financial challenges and eventually shut down in the 2010s. Their inability to scale profitability, along with technical and logistical issues, contributed to the closure.

## Slide 41: Superior Fresh Aquaponics
Largest aquaponics farm in the world
  Considered the Gold Standard for large-scale aquaponics operations
1st landlocked Atlantic salmon farm in the U.S. using RAS technologies
FCR = 1.1
(FCR = Feed Conversion Ratio)

## Slide 42: Superior Fresh Aquaponics
Grow leafy greens, herbs
  3 Million lbs. per year
State of the art greenhouses
Supplemental lighting for winter
Environmental parameters monitored and controlled

## Slide 43: Superior Fresh Aquaponics

## Slide 44: Recently closed aquaponics operations – Expanding land-based salmon operations

## Slide 45
The Aquaponics Paradigm
  Single greenhouse with leafy greens and tilapia has been the aquaponic model for decades
  Coupled system have been the norm where growers compromise on environmental variables to appease both fish and plants (I.e. pH =7)
  Problems:
  Difficult to compete with commodities market on leafy greens and other low-value crops
  Market for live fish is limited
  Not scalable
  High operating and startup costs
  The Paradigm Needs to Shift!
Notes: 18

## Slide 46
New Aquaponics Paradigm
  Hybrid models – Combine with traditional hydroponics
    RAS = Nutrient Factory
  Grow high-value crops (and diversify) – premium pricing (more different products per customer)
  Automation and AI monitoring –advanced nutrient sensors can improve efficiency
  Local and Specialty Markets – sell to restaurants, specialty markets, direct to consumers
Notes: 18

## Slide 47
Capable of saving even more water
Good solids filtration paramount to prevent clogging
Research forthcoming!

## Slide 48: Aeroponics Cannabis

## Slide 49
Other Innovative Strategies and Optimization Techniques
  Decoupling is a given
  Development of aquaponic-specific fish feeds
    Currently exploring unique insect larvae for which we can control diets to increase various nutrients (i.e. phosphorous, iron, calcium, potassium)
  Real-time monitoring of nutrient levels with automated addition of nutrients to maintain optimal balance

## Slide 50
Future Outlooks
  Currently exploring Microbiome and how it can be transferred into hydroponic operations
  Performing research on improving sludge digestion to increase nutrient content of Aquaponics effluent
  In process of developing insect-based aquaponic feed to promote more efficient plant growth

## Slide 51
Special Thanks to My Awesome Team of Students!
Interns
  Ashley Jeunke
  Jimmy McNeil
  Martin Rodriguez
  Angelo Mauro
  Jose Gallego
  Gia DeYoung
  Taylor McCoy
  Josiah Jackson
  Justin Smith
  Reese Arbitelle
  David Dong
  Desmond Traynor
  Jackson Schutter
  Tatyana Wong
  Curry Curry
  LJ Gusky
  Kennedy McEnany
  Ben Hunt
  Gracie Reinholz
Graduate Students
  Kate Stalkfleet
  Jessie Johnson
  Marcangelo Maisto
  Max Smith
  Lauren Stevenson
  Ryan Wheaton
  Rachel Nehrmeyer

## Slide 52: Questions?